## Slide 1
BU90007GWZ-E2EVK-101 Measurement Report
April 2nd, 2014
Hosted by: Xuan Dang

## Slide 2
Equipment list
Regulated DC Power Supply
  QJE QJ3005XE (0-30V/5A)
Multimeter:
  Fluke 87V True RMS
  Fluke 106
Oscilloscope
  Rigol DS1102E
Electronic Load
  B&K BK8500
Current probe
  RP1001C

## Slide 3
Functional Test
Test case 1 procedure
  Turn on the DC Supply. Set output of the DC Supply in range from 2.3V to 5.5V. Turn off the DC Supply. Connect DC Supply to: [+]VIN(TP1) and [-]GND(TP2).
  Set position of J2 header(Pin2 connect to Pin3) to select the IC operation mode is Automatic PFM/PWM mode.
  Connect Electronic Load to: [+]VOUT(TP3) and [-]GND(TP4). Power on Electronic Load, set input of Electronic Load to 1A and don’t turn on load.
  Move J1 header to turn EN on.
  Turn on the DC Supply.
  Turn on load.
Result:
VIN=2.3V to 5.5V, VOUT=1.247V
Follow datasheet, Output voltage accuracy is -2%/+3% (-0.025V/+0.0375V).
Test passed.

## Slide 4
Functional Test (cont.)
Test case 2 procedure
  Turn on the DC Supply. Set output of the DC Supply in range from 2.3V to 5.5V. Turn off the DC Supply. Connect DC Supply to: [+]VIN(TP1) and [-]GND(TP2).
  Set position of J2 header(Pin2 connect to Pin1) to select the IC operation mode is Forced PWM.
  Connect Electronic Load to: [+]VOUT(TP3) and [-]GND(TP4). Power on Electronic Load, set input of Electronic Load to 1A and don’t turn on load.
  Move J1 header to turn EN on.
  Turn on the DC Supply.
  Turn on load.
Result:
VIN=2.3V to 5.5V, VOUT=1.247V
Follow datasheet, Output voltage accuracy is ±2% (±0.025V).
Test passed.

## Slide 5
Functional Test (cont.)
Test case 3 procedure
  After implement test case 1, the IC operate properly.
  Move J1 header to turn EN off.
  Move J1 header to turn EN on.
Result:
VIN = 5V
VOUT = 0.25V/1A (in Automatic PFM/PWM Mode)
Test failed.
IOUT 500mA/Div. (DC)
VOUT 100mV/Div. (DC)

## Slide 6
Functional Test (cont.)
Test case 4 procedure
  After implement test case 2, the IC operate properly.
  Move J1 header to turn EN off.
  Move J1 header to turn EN on.
Result:
VIN = 5V
VOUT = 0.25V/1A (in Forced PWM Mode)
Test failed
IOUT 500mA/Div. (DC)
VOUT 100mV/Div. (DC)

## Slide 7
Functional Test (cont.)
Test case 5 procedure
  After implement test case 1, the IC operate properly.
  Turn off load.
  Turn on load.
Result:
VIN=5V, IOUT=100mA, VOUT=1.25V
Test passed.

## Slide 8
Functional Test (cont.)
Test case 6 procedure
  After implement test case 2, the IC operate properly.
  Turn off load.
  Turn on load.
Result:
VIN=5V, IOUT=1A, VOUT=1.247V
Test passed.

## Slide 9
Hot Plugging Test
Test condition
  VIN = 5.5V
  IOUT = 1A
  With original diode D1: P4SMA6.8A
Result:
IIN_PEAK= 14.3A
VIN peak transient voltage (in both modes) is 7.76V > VIN Maximum Rating (7V)
The IC still operate properly after 100+ testing time.
VIN 2V/Div. (DC)
IIN 3A/Div. (AC)

## Slide 10
Circuit Quiescent Current Measurement
Test condition
  VIN = 0-5.5V
  Automatic PFM/PWM Mode
  Room temperature 25oC
Chart: VCC (V)
| 0 | 0.25 | 0.5 | 0.6 | 0.7 | 0.73 | 0.74 | 0.75 | 1 | 1.1000000000000001 | 1.2 | 1.25 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.75 | 1.8 | 1.9 | 2 | 2.1 | 2.12 | 2.13 | 2.15 | 2.1749999999999998 | 2.2000000000000002 | 2.25 | 2.5 | 2.75 | 3 | 3.25 | 3.5 | 3.75 | 4 | 4.25 | 4.5 | 4.75 | 5 | 5.25 | 5.5
ICC With P4SMA6.8A | 0 | 0.2 | 0.3 | 0.4 | 0.5 | 0.5 | 0.6 | 0.6 | 60 | 130 | 228 | 290 | 346 | 419 | 495 | 560 | 630 | 661 | 697 | 740 | 760 | 767 | 44 | 44 | 44 | 44 | 44 | 44 | 46 | 47 | 48 | 50 | 52 | 54 | 57 | 60 | 64 | 68 | 75 | 84 | 98

## Slide 11
Circuit Quiescent Current Measurement (cont.)
Test condition
  VIN = 0-5.5V
  Forced PWM Mode
  Room temperature 25oC
Chart: VCC (V)
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 1.8 | 1.9 | 2 | 2.09 | 2.0990000000000002 | 2.1 | 2.2000000000000002 | 2.21 | 2.25 | 2.2999999999999998 | 2.4 | 2.5 | 2.75 | 3 | 3.25 | 3.5 | 3.75 | 4 | 4.25 | 4.5 | 4.75 | 5 | 5.25 | 5.5
ICC With P4SMA6.8A | 0 | 0.2 | 0.3 | 0.9 | 59 | 287 | 491 | 659 | 700 | 747 | 754 | 786 | 788 | 790 | 4870 | 4870 | 4880 | 4890 | 4960 | 4980 | 5140 | 5310 | 5430 | 5560 | 5710 | 5870 | 6040 | 6220 | 6410 | 6610 | 6840 | 7090

## Slide 12
Efficiency Measurements
Test condition
  VIN = 5V
  VOUT = 1.25V
  Room temperature 25oC
Chart: IOUT (mA)
| 0 | 10 | 20 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 120 | 125 | 130 | 140 | 150 | 160 | 180 | 200 | 225 | 250 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000
Automatic PFM/PWM | 0 | 74.6 | 78 | 80 | 80.6 | 81.3 | 81.8 | 82 | 82.2 | 82.4 | 82.3 | 82.3 | 82.3 | 79.7 | 79.1 | 79.8 | 80.7 | 81.1 | 81.8 | 82.1 | 82.5 | 81.9 | 81 | 79.9 | 78.4 | 77 | 75.3 | 73.6
Forced PWM Mode | 0 | 26.9 | 42.2 | 59 | 67.5 | 72.1 | 75.4 | 81.3 | 82.5 | 81.9 | 81 | 79.9 | 78.4 | 77 | 75.3 | 73.6

## Slide 13
Load Response Measurements
Load response characteristic
(VIN=5V, VOUT=1.25V, IOUT=0  1A, Automatic PFM/PWM Mode)
VOUT 20mV/Div. (AC)
IOUT 500mA/Div. (DC)

## Slide 14
Load Response Measurements (cont.)
Load response characteristic
(VIN=5V, VOUT=1.25V, IOUT=1A  0, Automatic PFM/PWM Mode)
VOUT 20mV/Div. (AC)
IOUT 500mA/Div. (DC)

## Slide 15
Load Response Measurements (cont.)
Load response characteristic
(VIN=5V, VOUT=1.25V, IOUT=0  1A, Forced PWM Mode)
VOUT 10mV/Div. (AC)
IOUT 500mA/Div. (DC)

## Slide 16
Load Response Measurements (cont.)
Load response characteristic
(VIN=5V, VOUT=1.25V, IOUT=1A  0, Forced PWM Mode)
VOUT 10mV/Div. (AC)
IOUT 500mA/Div. (DC)

## Slide 17
Ripple Response Measurements
VOUT Ripple voltage
(VIN=5V, VOUT=1.25V, IOUT=1A, Automatic PFM/PWM Mode and Forced PFM Mode)
VSW 2V/Div. (DC)
VOUT 10mV/Div. (AC)

## Slide 18
Ripple Response Measurements (cont.)
VOUT Ripple voltage
(VIN=5V, VOUT=1.25V, IOUT=10mA, Automatic PFM/PWM Mode)
VSW 2V/Div. (DC)
VOUT 20mV/Div. (AC)

## Slide 19
Ripple Response Measurements (cont.)
VOUT Ripple voltage
(VIN=5V, VOUT=1.25V, IOUT=0, Forced PWM Mode)
VSW 2V/Div. (DC)
VOUT 10mV/Div. (AC)

## Slide 20
Input Voltage Ripple Measurements
VIN Ripple voltage
(VIN=5V, VOUT=1.25V, CIN=4.7uF + 0.1uF, IOUT=10mA, Automatic PFM/PWM Mode)
VIN 20mV/Div. (AC)

## Slide 21
Input Voltage Ripple Measurements (cont.)
VIN Ripple voltage
(VIN=5V, VOUT=1.25V, CIN=4.7uF + 0.1uF, IOUT=0, Forced PWM Mode)
VIN 10mV/Div. (AC)

## Slide 22
Input Voltage Ripple Measurements (cont.)
VIN Ripple voltage
(VIN=5V, VOUT=1.25V, CIN=4.7uF + 0.1uF, IOUT=1A, Automatic PFM/PWM and Forced PWM Mode)
VIN 50mV/Div. (AC)